# Technical solution

# Program system AIRCAMD

(Cable Suspended Parallel Robot, CPR-D)

# Mirjana Filipovic,

# Mihailo Pupin Institute, University of Belgrade, Volgina 15, 11060 Belgrade, Serbia.

This research was supported by the Ministry of Education, Science and Technological Development, Government of The Republic of Serbia for financing the national research project “Ambientally intelligent service robots of anthropomorphic characteristics” TR-35003 and partially supported by the project: SNSF Care-robotics project no. IZ74Z0_137361/1.

# email:

# mira@robot.imp.bg.ac.rs                    mirjana.filipovic@pupin.rs

Figure1. CPR-D, in the 3D space.

This model is named CPR-D, and it is presented in Figs. 1 and 2.

This program system AIRCAMD introduces a novel mathematical model of the Aerial Robot (Cable-suspended Parallel Robot, CPR-D). This model is named CPR-D, and it is presented in Figs. 1 and 2. The novelty of the CPR model is the geometric relationship between the camera motion in the Cartesian coordinates (external coordinates) and motors angular positions in the joint coordinates (internal coordinates). This relationship is defined by the Jacobian matrix which is used for solving the kinematics and dynamics of the aerial robot. For the computation of the dynamic model, the Lagrange principle of virtual work is used. The Jacobian matrix used in the formulation of the Lagrange principle of virtual work has been adopted according to the construction of the mechanism of the aerial robot. The specific structures of the aerial robot play an important role in defining the kinematic and dynamic models of the CPR-D. The general form of the CPR-D mathematical model is defined. The modeling task is solved as software AIRCAMD so that a user should choose the system parameters that provide the possibility of the analysis of its dynamic behavior. There is a possibility of extension of program system AIRCAMD from different aspects. This program system is generated in MATLAB.

Figure2. CPR-D, top view.

# The area to which the technical solution refers

Synthesis and analysis of CPR-D system, Robotics, Theory of Mechanics.

Problem solved by technical solution

This technical solution solves the problem of efficient synthesis and analysis of aerial robot model in its construction, as well as testing its behavior under simulated real conditions of CPR-D system task realization.

# State of the problem solution in the world

One strong class of mechanisms used for different camera motions of CPR type has been developed strongly in last three decades. For three decades, researchers have dealt with the mechanisms that carry a camera for observation of the space or moving objects in space. Implementation of this system uses the latest technical knowledge. This is achieved using the latest computer, network and new types of motors, combined with confirmed high quality camera and video components.

Specially trained camera operator is responsible for process and quality recording. It is clear that for the full functioning of such a complex system must be responsible a team of experts of various profiles.

The modular design system for observation of workspace and light weight components and a small force in the ropes allow the successful setting up a system to almost any location, which offers wide possibilities for its use in closed or open space, which can be small or large sizes. It may be placed in the most unlikely places, for example when filmmaking of different genres or for military or police purposes.

Regardless of the purpose and in which areas the system installed, top priority is definitely a high safety of participants in the recorded event. In this sense, the system should get certified according to the highest European standards. The CPR system should fly over the audience without being able to be off and fall to the ground.

In the case of an emergency or failure, the security concept would immediately halt the system. The protection system works by activating all the brakes and the winches deactivated in milliseconds. Stopping the system can be run (provided) manually by the operator, by pressing one of the buttons provided for the alarming situation, or automatically by one of the integrated security protocols. The most important components of the security system are:

- a sensor that measures the force in each rope,

- rotating torque sensor, control unit for checking the winding,

- mechanical check of the brake functionality,

- continuous monitoring of the functionality of the brake contactor, motor contactor, servo-amplifiers, the stop commands to stop the system and fiber optic connections,
- continuous monitoring of the geometry and position of the camera carrier.

Each circuit has a double security system. In addition, there are two brakes for each winches, each brake is strong enough to respond quickly and to higher loads and no electricity. If a sudden cancellation of all motors, all brakes will be activated automatically.

Who first developed a CPR system? There are different claims. Source http://www.spidercam.net , the company Skycam claims that it was discovered in 1984 by Garrett Brown. Source http://broadcastengineering.com/infrastructure/cablecam , Broadcast Engineering firm claims to have discovered it in 1985 by Jim Rodnunsky. The source http://en.wikipedia.org/wiki/Spidercam writes that it was Jens C. Peters, a researcher from CCSytems Inc. It is certain that all of them are big names in this field because they contributed to the development of this system.

In its initial phase the system was used in limited circumstances that the technology's development allowed. Because of that its development has been slow, due to the support of computers technique. From that time until now the use of this system has been constantly expanding. During the transfer of sporting or other public events (football, basketball, hockey or other games, tennis or athletic competitions, Eurovision, concerts of various musical genres etc.) the presence of CPR system used for recording can be noticed. But in many areas this system has not yet appeared.

It should be noted here that the position of the camera is controlled via joystick by the operators, who are located to monitor the whole workspace with moving subjects. In this case the operator via the joystick moves the camera in all directions left, right, up, down etc. This system in its functioning depends on the concentration and the responsibility of the operators. Their skill and experience play a major role. Since the implementation of task observation of an event can last for hours, it's a pretty big responsibility for operators. Lack of concentration and their fatigue during the period indicates a significant dependence of this system on the human factor, which as a result can have a number of unavoidable inaccuracies during the operation.

Illogical assumption in the functioning of this system is that the relationship between the coordinates  , ,  is uniquely defined.

# The essence of the technical solution

Unlike previous approaches this program package proposes the application of theoretical methods in solving specific problems. This program system AIRCAMD has aims at using the mathematical model for CPR-D system according to the original scientific principles. In this program package the CPR-D system for tracking of moving objects is analyzed and synthesized. This may be a working hall or space for recording of cultural, sporting, exhibition or promotional events. Application possibilities are certainly much broader than it may be assumed at this moment, especially for military or police purposes. The analysis of existing solutions can provide distinguishing characteristics. The main contribution of this program system AIRCAMD can be defined in the following way.

The unique general type of the CPR-D mathematical model is defined. Kinematic model is generated for the system via Jacobian matrix. An adequate choice of generalized coordinates (in this paper, the internal coordinates), provides a mathematical model that illuminates the mapping of internal (resultant forces acting on the shaft of each motor) and external forces (acting on a camera carrier) by the Jacobian matrix on motion dynamics of each motor.

The presented CPR-D model is functionality generated by formulating and applying its highly authentic kinematic and dynamic model during synthesis and analysis which will enable further development and implementation of the current control laws. Software packages AIRCAMD is developed and used for individual and comparative analysis of the CPR-D from various aspects. The influence of changing any parameters of the system (workspace dimensions, the mass of a camera carrier, change the size and dynamics of power disturbances, the choice of control law, the reference trajectory, and the presence of singularity avoidance system and a number of other characteristics) can be analyzed through this software package.

The selection of the motor components is extremely important for the CPR-D performance. Motor type can significantly affect the response of the system or accuracy of the desired trajectory tracking.

The formulated program package AIRCAMD (based on its mathematical model) has a special significance because it is the foundation for further development and implementation of this system.

# Detailed features description

In this paper, a new original softver package AIRCAMD has been developed. Over the pulley CPR-D system, ropes are run on the winches (reel) 1, 2, 3, powered by motors. First and second motors are used to wind up the ropes about the coils. During the rotation one side is winding while another side is unwinding. The third motor is used to wind up the two ropes about the coil only in one direction. Those motion produce winding or unwinding of both ropes at the same time. This can be seen in Figures 2 and 3. Ropes coil on winches has radius .

Figure 3. a) The ropes forces before motor 1, motor 2 and motor 3 and after motor 1 and motor 2, b) The ropes forces which carry a camera (CPR-D).

Synchronous motion of the motors produce camera carrier to move in the , ,  Cartesian space. The desired motion trajectory of the camera is defined in , , , Cartesian coordinates, and it is generated by motion of three motors , , . The kinematic model of the CPR-D has been developed as essential part for solving the CPR-D dynamics. The relation between the camera motion in the Cartesian space, , and angular positions of each motor , ,  is solved by the Jacobi matrix , which connects velocities of external coordinates changes with velocities of internal coordinates changes. For generation of any trajectory in , ,  space, it is necessary to provide very precise and mutually coordinated motion of all three motors, , .

The Jacobian matrix  is not diagonal but full matrix. The elements of this matrix that are outside the diagonal show the strong coupling between the external and internal coordinates. The Jacobian matrix plays an important role in the generation of the system dynamic model too. In order to obtain the relationship between internal and external forces, the adapted Lagrange principle of virtual work can be applied. The mathematical model of CPR-D system is based on the Lagrange’s equation of motion using the generalized coordinates , , . Control law is selected by the local feedback loop for position and velocity of the motor shaft. See paper [1]. Program package AIRCAMD that is synthesized specially for the purpose of comfort analysis of such complex system served for obtaining simulation results. In order to make the results mutually comparable, the desired trajectory has been created and all needed system parameters. The camera carrier has starting point, and the end point . A camera carrier is under the influence of the disturbance force  Top of Form

, which simulates the impact of wind attack.

Oscillatory character of the responses presented on Fig. 5. Compare simulation results for all four constructions, CPR-A, CPR-B, CPR-C, and CPR-D, mutually.

By the comparative analysis of the results, we can come to the conclusion that these four CPR constructions follow the same trajectory of the camera carrier. It is important to notice that every construction has totally different motion of motors for the same camera trajectory. See technical solution for program systems AIRCAMA, AIRCAMB, AIRCAMC and paper [2].

Figure 4. The reference trajectory motion of a) position , , , b) velocity , , , c) velocity of the  of camera carrier (CPR-D).

Figure 5. Reference frame and real frame a) , , of camera carrier, b) , , of motor shaft, c) resultant forces acting on the shaft of each motor , real deviation from the reference frame values ​​of a motion trajectory of d) camera carrier, e) the motor shaft, f) Reference frame and real frame control signal  (CPR-D).

# Difference between these constructions is noticeable by the fact that they have different singular spaces, also. Analyzing the results of these four CPR constructions responses indicates their differences. For example, these differences are similar to those between four different industrial manipulators.

CPR-D system can be part of a more complex system as presented in [3].

# References

Mirjana Filipović, Ljubinko Kevac, „The Importanceof procedure of form a mathematical modl of aerial robot,” HIPNEM 2012, Belgrade, (October 18 2012). http://www.smeits.rs

M. Filipovic, Lj. Kevac and B. Reljin, “Comparative analysis of two configurations of aerial robot,“ 2012 SISY IEEE 10th Jubilee International Symposium on Intelligent Systems and Informatics, Subotica, Serbia, (September 20-22, 2012) 211-216, ISBN 978-1-4673-4750-1/12. http://conf.uni-obuda.hu/sisy2012/

A. Rodic, M. Jovanovic, S. Popic, G. Mester, Scalable Experimental Platform for Research, Development and Testing of Networked Robotic Systems in Informationally Structured Environments, Symposium Series on Computational Intelligence SSCI, Paris, France, (2011) 136-143.