# Technical solution

# Program system AIRCAMA

(Cable Suspended Parallel Robot, CPR-A)

# Mirjana Filipovic,

# Mihailo Pupin Institute, University of Belgrade, Volgina 15, 11060 Belgrade, Serbia.

This research was supported by the Ministry of Education, Science and Technological Development, Government of The Republic of Serbia for financing the national research project “Ambientally intelligent service robots of anthropomorphic characteristics” TR-35003 and partially supported by the project: SNSF Care-robotics project no. IZ74Z0_137361/1.

# email:

# mira@robot.imp.bg.ac.rs                    mirjana.filipovic@pupin.rs

Figure1. CPR-A, in the 3D space.

This program system is generated in MATLAB. In this program system a special case of the constructive aerial robot, Cable Suspended Parallel Robot - CPR model solution, has been analyzed. This chosen system is named CPR-A, and it is presented in Figs. 1 and 2. Program system AIRCAMA developed on this level can be used for synthesis and analysis of the CPR-A system and it can be expanded from different aspects, according to the users’ needs. Algorithm generates a proper definition of the system kinematic model which includes trajectory, velocity and acceleration is a prerequisite for the formulation of a dynamic model. These three components represent the basic functional criteria of the real system which is described by the corresponding geometric relations and differential equations. The unique and complex construction of the selected aerial robot requires in depth study of the novel methodology for developing its mathematical modeling. High fidelity mathematical model obtained by the multi-parameter accurate abstraction of a real system can be used to implement very complex tasks using the intelligent control systems. The modeling task is solved as software so that a user should choose the system parameters that provides the possibility of the analysis of its dynamic behavior. There is a possibility of extension of program system AIRCAMA from different aspects according to the users’ needs.

Figure2. CPR-A, top view.

# The area to which the technical solution refers

Synthesis and analysis of CPR-A system, Robotics, Theory of Mechanics.

Problem solved by technical solution

This technical solution solves the problem of efficient synthesis and analysis of aerial robot model in its construction, as well as testing its behavior under simulated real conditions of CPR-A system task realization.

# State of the problem solution in the world

One strong class of mechanisms used for different camera motions of CPR type has been developed strongly in last three decades. For three decades, researchers have dealt with the mechanisms that carry a camera for observation of the space or moving objects in space. Implementation of this system uses the latest technical knowledge. This is achieved using the latest computer, network and new types of motors, combined with confirmed high quality camera and video components.

Specially trained camera operator is responsible for process and quality recording. It is clear that for the full functioning of such a complex system must be responsible a team of experts of various profiles.

The modular design system for observation of workspace and light weight components and a small force in the ropes allow the successful setting up a system to almost any location, which offers wide possibilities for its use in closed or open space, which can be small or large sizes. It may be placed in the most unlikely places, for example when filmmaking of different genres or for military or police purposes.

Regardless of the purpose and in which areas the system installed, top priority is definitely a high safety of participants in the recorded event. In this sense, the system should get certified according to the highest European standards. The CPR system should fly over the audience without being able to be off and fall to the ground.

In the case of an emergency or failure, the security concept would immediately halt the system. The protection system works by activating all the brakes and the winches deactivated in milliseconds. Stopping the system can be run (provided) manually by the operator, by pressing one of the buttons provided for the alarming situation, or automatically by one of the integrated security protocols. The most important components of the security system are:

- a sensor that measures the force in each rope,

- rotating torque sensor, control unit for checking the winding,

- mechanical check of the brake functionality,

- continuous monitoring of the functionality of the brake contactor, motor contactor, servo-amplifiers, the stop commands to stop the system and fiber optic connections,
- continuous monitoring of the geometry and position of the camera carrier.

Each circuit has a double security system. In addition, there are two brakes for each winches, each brake is strong enough to respond quickly and to higher loads and no electricity. If a sudden cancellation of all motors, all brakes will be activated automatically.

Who first developed a CPR system? There are different claims. Source http://www.spidercam.net , the company Skycam claims that it was discovered in 1984 by Garrett Brown. Source http://broadcastengineering.com/infrastructure/cablecam , Broadcast Engineering firm claims to have discovered it in 1985 by Jim Rodnunsky. The source http://en.wikipedia.org/wiki/Spidercam writes that it was Jens C. Peters, a researcher from CCSytems Inc. It is certain that all of them are big names in this field because they contributed to the development of this system.

In its initial phase the system was used in limited circumstances that the technology's development allowed. Because of that its development has been slow, due to the support of computers technique. From that time until now the use of this system has been constantly expanding. During the transfer of sporting or other public events (football, basketball, hockey or other games, tennis or athletic competitions, Eurovision, concerts of various musical genres etc.) the presence of CPR system used for recording can be noticed. But in many areas this system has not yet appeared.

It should be noted here that the position of the camera is controlled via joystick by the operators, who are located to monitor the whole workspace with moving subjects. In this case the operator via the joystick moves the camera in all directions left, right, up, down etc. This system in its functioning depends on the concentration and the responsibility of the operators. Their skill and experience play a major role. Since the implementation of task observation of an event can last for hours, it's a pretty big responsibility for operators. Lack of concentration and their fatigue during the period indicates a significant dependence of this system on the human factor, which as a result can have a number of unavoidable inaccuracies during the operation.

Illogical assumption in the functioning of this system is that the relationship between the coordinates  , ,  is uniquely defined.

# The essence of the technical solution

Unlike previous approaches this program package proposes the application of theoretical methods in solving specific problems. This program system AIRCAMA has aims at using the mathematical model for CPR-A system according to the original scientific principles. In this program package the CPR-A system for tracking of moving objects is analyzed and synthesized. This may be a working hall or space for recording of cultural, sporting, exhibition or promotional events. Application possibilities are certainly much broader than it may be assumed at this moment, especially for military or police purposes. The analysis of existing solutions can provide distinguishing characteristics. However, regardless of the chosen type of solution, it is of particular importance to establish the geometric relationship between the camera motions in the space of Cartesian coordinates and motors motion. This geometric relationship allows the formulation of highly fidelity kinematic and dynamic models of CPR-A system for capturing moving objects. The mathematical model defines of camera motions in space to monitor moving objects in the respective zone. The software package AIRCAMA is also synthesized for the same purpose, and it offers a choice of parameters of the system and analysis of its dynamic behavior as well as with the purpose of presenting comparative results. Defined algorithm is applied to any size workspace selection, with the weight of CPR-A system, the desired speed cameras and so on. Depending on the choice of these parameters types and characteristics of each engine are chosen. Activating the program package, it is possible to make the analysis of the results, where it can be concluded if the selection of motor types is correct, or whether it meets the requirements. It is also possible to analyze the coordination of motion in relation to the desired requests. It is possible to observe any motion from the selected workspace. The formulated program package AIRCAMA (based on its mathematical model) has a special significance because it is the foundation for further development and implementation of this system.

# Detailed features description

Such system is primarily very useful, expensive and demanding during the operation.

Program package that can be used for synthesis and analysis of CPR-A system is synthesized in this program package AIRCAMA and it can also be upgraded and expanded from different aspects.

Figure 3. a) The ropes forces before motor 1, motor 2 and motor 3 and after motor 1 and motor 2, b) The ropes forces which carry a camera (CPR-A).

Motion of the ropes which carry the camera is controlled. Ropes are unwound (or wound), thus reaching any camera position in space. The control system has the operating software, which as a result provides three-dimensional motion of the camera. The commands for the synchronized motion of each winch are provided, with control of motion of each motor, which ultimately provides three-dimensional continuous camera motion. Real-time communication between the winches and the control module is achieved via a cable. Can be used two optical cables that allow dual processing of information. Motors receive and implement the information from the control station, over winches. The camera transmits their HD signal back to the control station. The carrier that carries the camera does not have a role only of mechanical motion, because through it remote lens (focus, zoom and clarity) is controlled. The gyro sensor, which is installed in the carrier, is stabilized towards the horizon.

CPR-A system, has a suspension system in four points, i.e. to be hung on all four edges of the workspace shape parallelepiped. It is a necessary geometric condition so as to provide camera motion through the entire space. The whole CPR system operates as shown, using two ropes and pulleys that are fixed for up to four corners of point’s space observation. See Fig. 1 and 2. The whole system is very reliable in the physical sense, because there is only minimal possibility that the camera carrier falls to the shot ground. This would happen only if both ropes broke at the same time. Two parallel guided ropes through the system are inevitable for the physical functioning of the system in Fig. 1 and 2. In the event when one rope breaks, the system ceases to function, but by definition the second rope will not give the opportunity to carrier that the camera falls to the ground and to hurt anyone. This type of construction, by definition, guarantees the safety of participants in the workspace. Through the system of pulleys, ropes are kept on winches 1, 2, 3, that are driven by motors. Ropes are winding on the winches of radius  or they are unwinding from them. Video from the camera is sent to the user via a separate fiber-optic cable. Winch 4 is driven by a motor that realizes the motion  reeling or unwinding fiber-optic cable, depending on the position of a camera carrier in the space. The purpose of moving the motor  is to ensure that the fiber-optic cable is never tight or too laid back to come down too much overhead above the recorded surface and thus interfere with the participants recorded. This trend is now also controlled by the operator using a joystick, which is located so that at any time following the tension fiber-optic cable in relation to the camera carrier. Namely in order to realize the desired motion in the  direction, motion of the motor  is not enough, also in order to realize the desired motion in the  direction, motion of the motor  is not enough, and finally to realize the desired motion in the  direction, motion of the motor  is not enough. There is a strong coupling between the motion of the camera in the space of Cartesian coordinates , ,  and rotation angles of each motor, , . This relationship is clearly defined by the Jacobian matrix , which connects the external velocity of change of coordinates with the velocity of change of internal coordinates . It is significantly more complicated than the experts from http://www.spidercam.net assumed. For the realization of any trajectory in , ,  space, it is necessary to provide very precise and mutually coordinated motion of all three motors, , . The Jacobian matrix  is not diagonal but full matrix. The elements of this matrix that are outside the diagonal show the strong coupling between the external and internal coordinates. The Jacobian matrix plays an important role in the generation of the system dynamic model too. In order to obtain the relationship between internal and external forces, the adapted Lagrange principle of virtual work can be applied. The mathematical model of CPR-A system is based on the Lagrange’s equation of motion using the generalized coordinates , , . Control law is selected by the local feedback loop for position and velocity of the motor shaft. See papers [1]-[6]. The CPR-A system is in a process of developing at the Mihajlo Pupin Institute [7]. Program package AIRCAMA that is synthesized specially for the purpose of comfort analysis of such complex system served for obtaining simulation results. In order to make the results mutually comparable, the desired trajectory has been created and all needed system parameters. The camera carrier has starting point, and the end point . A camera carrier is under the influence of the disturbance force  Top of Form

, which simulates the impact of wind attack.

Figure 4. The reference trajectory motion of a) position , , , b) velocity , , , c) velocity of the  of camera carrier (CPR-A).

Figure 5. Reference frame and real frame a) , , of camera carrier, b) , , of motor shaft, c) resultant forces acting on the shaft of each motor , real deviation from the reference frame values ​​of a motion trajectory of d) camera carrier, e) the motor shaft, f) Reference frame and real frame control signal  (CPR-A).

Oscillatory character of the responses presented on Fig. 5. Compare simulation results for all four constructions, CPR-A, CPR-B, CPR-C, and CPR-D, mutually.

# By the comparative analysis of the results, we can come to the conclusion that these four CPR constructions follow the same trajectory of the camera carrier. It is important to notice that every construction has totally different motion of motors for the same camera trajectory. See technical solution for program systems AIRCAMB, AIRCAMC, AIRCAMD and paper [5]. Difference between these constructions is noticeable by the fact that they have different singular spaces, also. Analyzing the results of these four CPR constructions responses indicates their differences. For example, these differences are similar to those between four different industrial manipulators.

# References

M. Filipovic, S. Popic, M. Jovanovic i A. Rodic: “Workspace observation system”, 24. International Congress on Process Industry, PROCESING 2011, Fruška Gora, SMEITS, ISBN 978-86-81505-61-8, 01-03, Jun 2011. http://www.snmeits.rs

M. Filipović, “Coupling between motor motion of Cable-suspended Parallel Robot”, INFOTEH-JAHORINA, Bosnia and Herzegovina, Vol 11, 21-23 March 2012, pp. 481-486. http://www.infoteh.rs.ba/indexe.php?strana=rad_prijavljeni&sesija=3

Mirjana Filipović, „The Importance of Modelling an Aerial Robotic Camera”, Scientific – Technical Review, Military Technical Institute, Belgrade, ISSN 1820-0206, 2012, Vol. 62, No. 1, pp. 28-37. http://www.vti.mod.gov.rs/ntp

M. Filipovic, „Analysis and synthesis of aerial robot”, Proceedings of 56. Serbian Conference for ETRAN, Zlatibor, 11 - 14. jun 2012, RO ISBN 978-86-80509-66-2. http://etran.etf.rs/

M. Filipovic, Lj. Kevac and B. Reljin, “Comparative analysis of two configurations of aerial robot,“ 2012 SISY IEEE 10th Jubilee International Symposium on Intelligent Systems and Informatics, Subotica, Serbia, (September 20-22, 2012) 211-216, ISBN 978-1-4673-4750-1/12. http://conf.uni-obuda.hu/sisy2012/

M. Filipovic, A. Djuric, Lj. Kevac “Contribution to the modeling of Cable-suspended Parallel Robot hanged on the four points”, IROS 2012: IEEE/RSJ International Conference on Intelligent Robots and Systems, Vilamoura, Portugal (October 7-12, 2012) 3526-3531. ISBN 978-1-4673-1735-1. http://www.iros2012.org/site/

A. Rodic, M. Jovanovic, S. Popic, G. Mester, Scalable Experimental Platform for Research, Development and Testing of Networked Robotic Systems in Informationally Structured Environments, Symposium Series on Computational Intelligence SSCI, Paris, France, (2011) 136-143.