# Technical solution

# Program system ORIGI

(for RSCPR system, Rigid ropes S-type Cable-suspended Parallel Robot)

# Mirjana Filipovic,

# Mihailo Pupin Institute, University of Belgrade, Volgina 15, 11060 Belgrade, Serbia.

This research was supported by the Ministry of Education, Science and Technological Development, Government of The Republic of Serbia for financing the national research project “Ambientally intelligent service robots of anthropomorphic characteristics” TR-35003 and partially supported by the project: SNSF Care-robotics project no. IZ74Z0_137361/1.

# email:

# mira@robot.imp.bg.ac.rs                    mirjana.filipovic@pupin.rs

Figure1. RSCPR, in the 3D space.

This program system is generated in MATLAB. This program system presents the analysis, synthesis and modeling of the selected Rigid ropes S-type Cable-suspended Parallel Robot (RSCPR). The important characteristic of this system is its geometric construction which defines the kinematic model through the Jacobian matrix. The relationship between external and internal forces is defined by the Lagrange principle of virtual work. The Jacobian matrix is directly involved in the application of the Lagrange principle of virtual work and generation of the dynamic model of the RSCPR system. Different examples of the RSCPR system are analyzed and their results are presented. The software packages named ORIGI has been used for the RSCPR model verification.

Figure2. RSCPR, top view.

# The area to which the technical solution refers

Synthesis and analysis of RSCPR system, Robotics, Theory of Mechanics.

Problem solved by technical solution

This technical solution solves the problem of efficient synthesis and analysis of aerial robot model in its construction, as well as testing its behavior under simulated real conditions of RSCPR system task realization.

# State of the problem solution in the world

One strong class of mechanisms used for different camera motions of CPR type has been developed strongly in last three decades. For three decades, researchers have dealt with the mechanisms that carry a camera for observation of the space or moving objects in space. Implementation of this system uses the latest technical knowledge. This is achieved using the latest computer, network and new types of motors, combined with confirmed high quality camera and video components.

Specially trained camera operator is responsible for process and quality recording. It is clear that for the full functioning of such a complex system must be responsible a team of experts of various profiles.

The modular design system for observation of workspace and light weight components and a small force in the ropes allow the successful setting up a system to almost any location, which offers wide possibilities for its use in closed or open space, which can be small or large sizes. It may be placed in the most unlikely places, for example when filmmaking of different genres or for military or police purposes.

Regardless of the purpose and in which areas the system installed, top priority is definitely a high safety of participants in the recorded event. In this sense, the system should get certified according to the highest European standards. The CPR system should fly over the audience without being able to be off and fall to the ground.

In the case of an emergency or failure, the security concept would immediately halt the system. The protection system works by activating all the brakes and the winches deactivated in milliseconds. Stopping the system can be run (provided) manually by the operator, by pressing one of the buttons provided for the alarming situation, or automatically by one of the integrated security protocols. The most important components of the security system are:

- a sensor that measures the force in each rope,

- rotating torque sensor, control unit for checking the winding,

- mechanical check of the brake functionality,

- continuous monitoring of the functionality of the brake contactor, motor contactor, servo-amplifiers, the stop commands to stop the system and fiber optic connections,
- continuous monitoring of the geometry and position of the camera carrier.

Each circuit has a double security system. In addition, there are two brakes for each winches, each brake is strong enough to respond quickly and to higher loads and no electricity. If a sudden cancellation of all motors, all brakes will be activated automatically.

Who first developed a CPR system? There are different claims. Source http://www.spidercam.net , the company Skycam claims that it was discovered in 1984 by Garrett Brown. Source http://broadcastengineering.com/infrastructure/cablecam , Broadcast Engineering firm claims to have discovered it in 1985 by Jim Rodnunsky. The source http://en.wikipedia.org/wiki/Spidercam writes that it was Jens C. Peters, a researcher from CCSytems Inc. It is certain that all of them are big names in this field because they contributed to the development of this system.

In its initial phase the system was used in limited circumstances that the technology's development allowed. Because of that its development has been slow, due to the support of computers technique. From that time until now the use of this system has been constantly expanding. During the transfer of sporting or other public events (football, basketball, hockey or other games, tennis or athletic competitions, Eurovision, concerts of various musical genres etc.) the presence of CPR system used for recording can be noticed. But in many areas this system has not yet appeared.

It should be noted here that the position of the camera is controlled via joystick by the operators, who are located to monitor the whole workspace with moving subjects. In this case the operator via the joystick moves the camera in all directions left, right, up, down etc. This system in its functioning depends on the concentration and the responsibility of the operators. Their skill and experience play a major role. Since the implementation of task observation of an event can last for hours, it's a pretty big responsibility for operators. Lack of concentration and their fatigue during the period indicates a significant dependence of this system on the human factor, which as a result can have a number of unavoidable inaccuracies during the operation.

Illogical assumption in the functioning of this system is that the relationship between the coordinates  , ,  is uniquely defined.

# The essence of the technical solution

Unlike previous approaches this program package proposes the application of theoretical methods in solving specific problems. This program system ORIGI has aims at using the mathematical model for RSCPR system according to the original scientific principles. In this program package the RSCPR system for tracking of moving objects is analyzed and synthesized. This may be a working hall or space for recording of cultural, sporting, exhibition or promotional events.

The advantage of the RSCPR system is that the camera carrier moves in the working space of the parallelepiped shape, which is powered by three ropes, three coils and driven by three motors. This system has four pivot points used to determine the workspace shape. The camera motion in 3D space is controlled by three motors, which means that the system is not redundant. The RSCPR has simple and cheap construction.

The geometric relations between the motor and the camera motion are highly important for the kinematic and dynamic modeling of the system.

The generalized coordinates selected for the RSCPR model are motors angular positions , ,  named internal coordinates. The camera carrier motion is defined in the Cartesian space, described with the , ,  coordinates, named external coordinate system. The relation between internal and external coordinates is described by the Jacobian matrix .

The relation between the forces in the ropes and the forces acting at the camera carrier is solved by using a well-known Lagrange principle of virtual work.

This calculation shows the significance of the Jacobian matrix.

The resulting equation developed by the Lagrange principle of virtual work has been used for determining the dynamic model of the RSCPR system. This calculation shows the influence of the external force on the motor dynamics.

The software package ORIGI has been developed and used for individual analysis of the RSCPR model from various aspects such as selecting different workspace dimensions, a camera carrier mass, the external disturbances, the choice of the control law, the reference trajectory, the singularity avoidance and many other characteristics.

It is also possible to analyze the coordination of motion in relation to the desired requests. It is possible to observe any motion from the selected workspace. The formulated program package ORIGI (based on its mathematical model) has a special significance because it is the foundation for further development and implementation of this system.

# Detailed features description

The graphical representation of the RSCPR is shown in Fig. 1 and 2.

The camera carrier of the RSCPR structure is guided through the work area of the parallelepiped shape with three ropes connected with three winches, each powered by the motors.

The ropes of the pulley system are run on the winches (reel) 1, 2, 3, powered by the motors. The ropes coil or uncoil on the winches of radius , , and . The motors rotate winches directly and its angular positions are , , and . This motion moves the camera in the , ,  Cartesian coordinates.

Figure 3. The ropes forces which carry a camera (RSCPR).

The first step towards the dynamic model of the RSCPR is the development of its kinematic model. This calculation involves accurate definition of the geometric relationship between the camera motion in the , ,  Cartesian space (external coordinates) and motor angular positions , , , (internal coordinates).

The relation between the internal and external coordinates is defined by the Jacobian matrix , which relates the velocities of the external coordinates with the velocities of the internal coordinates . For the generation of any trajectory in , ,  space, it is necessary to provide very precise and mutually coordinated motion of all three motors, , .

The 3D recorded space has a parallelepiped shape of length , width , and height . In this 3D space it can be seen that the camera is connected with the ropes. See Fig. 2. The connecting dimensions are , , , . These dimensions are very small in comparison with the complete 3D recorded space. From this observation it is clear that , , , . It is also assumed that the pivot point A at height  is equal to the heights of all three connecting points.

This fact allows us to choose a point  as a hanging position of the camera carrier for all three ropes, see Figure 2. This camera carrier system can be easily constructed. This assumption simplifies the definition of geometric relations between camera carrier motion in Cartesian coordinates and coordinated motions of all motors.

By this approach, the new research prospects have been opened.

Emphasis is placed on the importance of these results in the field of robotics, which develops very extensively and it becomes the inspiration in this research for the development of areas such as dynamics of nonlinear phenomena of RSCPR structures and its stability.

Program package ORIGI that is synthesized specially for the purpose of comfort analysis of such complex system served for obtaining simulation results and validation theoretical contributions.